The International System of Units

| SI Base Units |
| --- |
| Quantity | Name | Symbol | Definition of Unit |
| Length | Metre | m | The metre is the length of the path travelled by light in vacuum during a time interval of 1/299 792 458 of a second |
| Mass | Kilogram | kg | The mass of the international prototype of the kilogram, kept at the International Bureau of Weights and Measures. |
| Time | Second | s | The second is the duration of 9 192 631 770 periods of the radiation corresponding to the transition between the two hyperfine levels of the ground state of the caesium 133 atom. |
| Electric current | Ampere | A | The ampere is that constant current which, if maintained in two straight parallel conductors of infinite length, of negligible circular cross-section, and placed 1 meter apart in vacuum, would produce between these conductors a force equal to 2 x 10-7 Newton per meter of length. |
| Thermodynamic temperature | Kelvin | K | The Kelvin, unit of thermodynamic temperature, is the fraction 1/273.16 of the thermodynamic temperature of the triple point of water – the equilibrium temperature between pure ice, airfree water and water vapour. |
| Amount of substance | Mole | mol | 1. The mole is the amount of substance of a system which contains as many elementary entities as there are atoms in 0.012 kilogram of carbon 12. |
| Luminous intensity | candela | cd | The candela is the luminous intensity, in a given direction, of a source that emits monochromatic radiation of frequency 540×1012 hertz and that has a radiant intensity in that direction of 1/683 watt per steradian. |

| SI Prefixes |
| --- |
| Multiplying Factor | Name of prefix | Symbol for prefix |
| 1018 | exa | E |
| 1015 | peta | P |
| 1012 | tera | T |
| 109 | giga | G |
| 106 | mega | M |
| 103 | kilo | k |
| 102 | hecto | h |
| 101 | deca | da |
| 10-1 | deci | d |
| 10-2 | centi | c |
| 10-3 | milli | m |
| 10-6 | micro | µ |
| 10-9 | nano | n |
| 10-12 | pico | p |
| 10-15 | femto | f |
| 10-18 | atto | a |

# Text boxes

| Some Units Permitted for Use with SI |
| --- |
| Quantity | Name | Symbol | Definition |
| time | Minute | min | 1 min = 60 s |
|  | Hour | h | 1 h = 3600 s |
|  | Day | d | 1 d = 86400 s |
|  | Year | a | 1 a = 365.24 d (approx) |
| volume | litre | L | 1 L = 1 dm3 (10-2 m3) |
| temperature | degree Celsius | oC | 0 oC = 273.15 K For intervals 1 oC = 1 K |
| mass | tonne | t | 1 t = 1000 kg |
| energy | electron volt | eV | 1 eV = 0.160219 aJ (approx) |
| mass of an atom | Unified atomic mass unit | u | 1 u = 1.6605655x10-27 kg (approx) |