## Slide 1: Series and Parallel Circuits

## Slide 2
The two simplest ways to connect conductors and load are series and parallel circuits.
Series circuit - A circuit in which loads are connected one after another in a single path.
Parallel circuit – A circuit in which loads are connected side by side.

## Slide 3: Gustav Robert Kirchhoff
Each arrangement affects the way in which potential difference and current act in the various parts of the circuit. Gustav Robert Kirchhoff studied the way each of the circuit parameters behaved in series and parallel circuits. His research led to two laws.

## Slide 4: Kirchhoff’s current law
the total amount of current into a junction point of a circuit equals the total current that flows out of that same junction.

## Slide 5
In the diagram to blow, three branches are coming together at one junction point and two branches leave. I1 + I2 + I3 = I4 + I5

## Slide 6: Kirchhoff’s Voltage Law
The total of all electric potential difference in any complete circuit loop is equal to any potential increases in the circuit loop.

## Slide 7
The potential increase, VT is equivalent to the sum of all the potential losses so that
VT = V1 + V2 + V3
V1
V2
V3
VT

## Slide 8
Kirchhoff’s laws are particular applications of the laws of conservation of electric charge and the conservation of energy.
In any circuit, there is no net gain or loss of electric charge or energy.

## Slide 9: Example1: Kirchhoff’s law in a series circuit
A simple series circuit is seen below. Use Kirchhoff’s current and voltage laws to find the values of the missing voltage (V2) and current (I2)
R2
R1
I3
10.0 A
30 V
V2
30 V
100v
10.0 A
10.0 A

## Slide 10: Voltage
according to Kirchhoff’s law, this series circuit has one voltage increase of 100V. This voltage must be distributed so that the sum of all voltage drops for each individual resistor must equal this value.

## Slide 11
VT = V1 + V2 + V3
So V2 = VT – V1 – V3
V2 = 100 V – 30 V – 30 V
= 40 V
R2
R1
I3
10.0 A
30 V
V2
30 V
100v
10.0 A
10.0 A

## Slide 12: Current
According to Kirchhoff’s current law, this series circuit has no real junction point, so it has only one path to follow. Therefore,

## Slide 13
IT = I1 = I2 = I3 =
IT = 10 A
R2
R1
I3
10.0 A
30 V
V2
30 V
100v
10.0 A
10.0 A

## Slide 14: Example 2: Kirchhoff’s laws in a parallel circuit
A simple parallel circuit shown below shows how Kirchhoff’s current and voltage laws can be used to find the missing voltage (V2) and current (I3).
9.0 A
I3
3.0 A
3.0 A
R3
R2
R1
30V
30V
30V
V2

## Slide 15: Voltage
The voltage increase is 30 V, thus there must be a decrease for each of the three different parallel resistor paths. Therefore, VT = V1 = V2 = V3
The voltage drop across all three parallel resistors is 30 V, no matter what their resistances.
9.0 A
I3
3.0 A
3.0 A
R3
R2
R1
30V
30V
30V
V2

## Slide 16: Current
There are 4 junction points in this diagram. One at the top and bottom of each branch, to resistors 1 and 2. The sum of the current entering the junctions must equal the sum exiting.
9.0 A
I3
3.0 A
3.0 A
R3
R2
R1
30V
30V
30V
V2

## Slide 17
IT = I1 + I2 + I3 = 9 A
I3 = IT – I1 – I2 = 9 A – 3 A – 3A
= 3A

## Slide 18: Resistance in series
In a series circuit, all current must first pass through resistor 1, then 2, and so on. The voltage drops across each resistor. The sum of the voltage drops gives the overall voltage drop in the circuit.
R2
R1
R3
10.0 A
30 V
V2
30 V
100v
10.0 A
10.0 A

## Slide 19
From Kirchhoff’s law, VT = V1 + V2 + V3
From Ohm’s law, ITRT = I1R1 + I2R2 + I3R3
But from Kirchhoff’s law, IT = I1 = I2 = I3
The currents factor out; IRT = IR1 + IR2 + IR3
Therefore, RT = R1 + R2 + R3
If all the resistors are the same, use the formula

## Slide 20: Example 3: Resistors in series
What is the series equivalent resistance of 10 Ω, 20 Ω, and 30 Ω resistors connected in series?
RT = R1 + R2 + R3
Therefore, RT = 10 Ω + 20 Ω + 30 Ω
= 60 Ω.
R2
R1
R3
10.0 A
30 V
V2
30 V
100v
10.0 A
10.0 A

## Slide 21: Resistance in parallel
In a parallel circuit, the total current must split and distribute its self among all of the available circuit paths.
From Kirchhoff’s law, IT = I1 + I2 + I3
From Ohm’s law
But from Kirchhoff’s law VT = V1 = V2 = V3
The voltages factor out
Therefore,

## Slide 22
If all the resistors are the same, use the formula
9.0 A
I3
3.0 A
3.0 A
R3
R2
R1
30V
30V
30V
V2

## Slide 23: Example: Resistors in parallel
What is the parallel equivalent resistance for a 25 Ω, 40 Ω, and 10 Ω resistors wired in parallel?

## Slide 24
Therefore,

## Slide 25
This can calculated easily on the calculator by using the fraction button.
  a b/c button
= 33/200
RT = 200 / 33 = 6.1

## Slide 26: Questions
Calculate the total resistance for the following:
  Three resistors, each 20 Ω, connected in series
  Three resistors, each 20 Ω, connected in parallel
Calculate the total current in a parallel circuit with current of I1 = 2.1 A in resistor 1, I2 = 3.1 in resistor 2 and I3 = 4.2 in resistor 3.
Calculate the total potential difference in a series circuit with a potential difference of V1 = 12 V in resistor 1, V2 = 14 V in resistor 2 and V3 = 16 V in resistor 3.
Calculate the equivalent resistance of a circuit with the flowing resistors in parallel: 5 Ω, 10 Ω, and 30 Ω.
A 1.0 Ω resistor is hooked up to a 1.0 x 106 Ω resistor in a) series , b) parallel. For each situation, calculate the total resistance and explain the dominance of one resistor in the total value.